## Slide 1: Module5
Randomization
Text book: Chris Spear

## Slide 2: Randomization Overview
  As designs grow it becomes more difficult to test their features through directed test cases
  Directed test cases checks specific features of a design and can only detect anticipated bugs
  Directed test case approach is a time consuming exercise
  Directed tests detect only anticipated bugs in the design
Why Randomize?
Random testing detects the bugs you did not expect in your design
Solution is Constrained Random Testcases (CRT) which randomize the input stimulus

## Slide 3: Randomization
Randomization is the process of making something random.
SystemVerilog randomization is the process of generating random values to a variable.
Verilog has a $random method for generating the random integer values-this is good for randomizing the variables alone, but it is hard to use in case of class object randomization.
For easy randomization of class properties, SystemVerilog provides rand keyword and randomize() method.

## Slide 4: What to Randomize?
Device configurations
  Try different device configurations
  For instance for a switch verification try different configurations of input and output ports
Environment configurations
  Randomize the entire environment that the device operates in
    The number of objects
    Object configurations
  For instance randomize the number of PCI busses connected to a particular device

## Slide 5: Test Bench

## Slide 6: What to Randomize?
Primary Input Data
  Randomize input data
  Constrain the inputs to be within valid limits
Encapsulated input data
  If the data is encapsulated, the different layers of encapsulation should be randomized and the device should be tested with different input configurations
  The encapsulated data should also be randomized

## Slide 7: What to Randomize?
Protocol exceptions, errors and violations
  Verify how system handles errors
  Anticipate error cases and inject into the system to ensure that the design gracefully handles them
  Inject errors randomly
Delays
  Use random legal delays specified by the protocols
  Check for clock jitter sensitivity
  Do not try to violate set up and hold requirements

## Slide 8
random variables: The class variables which get random values on randomization are called random variables.
In order to make variables as random variables, Class variables need to be declared using the rand and randc type-modifier keywords.
Following types can be declared as rand and randc,
--singular variables of any integral type
--arrays
--arrays size
--object handle’s

## Slide 9
Ex: rand bit [3:0] addr;
addr is a 4-bit unsigned integer with a range of 0 to 15. on randomization this variable shall be assigned any value in the range 0 to 15 with equal probability
randc keyword
randc is random-cyclic. For the variables declared with the randc keyword, on randomization variable values don’t repeat a random value until every possible value has been assigned.

## Slide 11
randomization example
In the previous example, Two variables addr1 and addr2 of same bit type are declared as rand and randc respectively, observe the randomized values of addr1 and addr2.
addr1 – takes the random value on every randomization addr2 – takes the random value on every randomization, but takes random value until every possible value has been assigned

## Slide 12
In order to randomize the object variables, the user needs to call randomize() method.
example: object.randomize()

## Slide 13: Randomization in SystemVerilog
Overview
  Randomization enables users to automatically generate random input stimulus for functional verification
  SystemVerilog enables user to specify random constrained (legal) values
  Random constraints should be specified using OOP

## Slide 14: Randomization in SystemVerilog
rand keyword
  Random variables are declared with the rand keyword
    Their values are uniformly distributed over the specified range
    If unconstrained the variable shall assign any value in the specified range with equal probability
rand bit [7:0] y;
8-bit unsigned integer with the range 0 to 255
The probability of the same value repeating on successive calls to randomize is 1/256
If unconstrained y is assigned any value in the range 0 to 255 with equal probability
The probability of a value occurring on simultaneous calls to randomize is 1/256

## Slide 15: Randomization in SystemVerilog
randc keyword
  Random cyclic variables are declared with the randc keyword
    They cycle through all the values in a random permutation of their declared range
    Can only be of the type bit or enum
    randc randomly iterates over all the values in the range and no value is repeated within an iteration
      When the iteration finishes, a new iteration automatically starts
randc bit [1:0] y;
2-bit unsigned integer with the range 0 to 3
y can take values 0,1,2,3
initial permutation 0 -> 3 -> 2 -> 1
next permutation 2 -> 1 -> 3 -> 0
next permutation 2 -> 0 -> 1 -> 3

## Slide 16: Randomization in SystemVerilog
Simple class with random variables
  The Bus class models a simplified bus with two random variables: addr and data
  The range1 constraint specifies the limits for the values of addr
    Ensure non conflicting and legal constraints
class Bus
rand bit[15:0] addr;
randc bit[31:0] data;
constraint range1 {addr>1024; addr<16384;}
endclass
random variable
random cyclic: the random solver
will not repeat a permutation of values
constraining the random variables to values between 1024 and 16384
Example: Simple class with random variables

## Slide 17: Randomization in SystemVerilog
Bus bus=new;
repeat (50) begin
if(bus.randomize()==1)
$display(bus.addr, bus.data);
else
$display (“Randomization failed”);
end
a bus object is created and
randomized 50 times
randomize()function
  Calling randomize() causes new values to be selected for all of the random variables in an object
    The random values obey the constraints
  randomize function returns a 1 on success and 0 on failure
  Unconstrained variables are assigned any values in their declared range
result of each randomization
is checked
Example: randomize() function example

## Slide 18: Randomization in SystemVerilog
The constraint solver
  Solves constraint expressions
  The same seed results in the same random values
    Use a different seed to generate different set of random values
  The solver is specific to the simulation vendor

## Slide 19: Constraint Details
Constraint Blocks
  Values of random variables are determined using constraint expressions that are declared using constraint blocks
    Smart stimulus tests relationships between variables
  They are class members like tasks, functions and variables
  Constraint declaration
    Constraint identifier: is the name of the constraint block.
    Constraint block: is a list of expression statements that restrict the range of variable or define relations between variables
class Bus
bit[15:0] addr;
randc bit[31:0] data;
constraint range1 {addr>1024; addr<16384;}
endclass
Error!!!
rand bit[15:0] addr;
constraint_identifier
constraint_block
In the example below randomize() fails sometimes and succeeds sometimes, why?
Example: Simple constraint example

## Slide 20: Constraint Details
Simple expressions
  Constraint variables have to be in a fixed order
    There can be only one relational operator (<, <=, ==, >= or >)
    For multiple variables use multiple expressions
class Bus
rand bit[15:0] a,b,c;
constraint c1 { 0 < a < b < c; }
endclass
Declare a constraint to solve: 0 < a < b < c
class Bus
rand bit[15:0] a,b,c;
constraint c1 { 0 < a;
a < b;
b < c;}
endclass
Error!!! wrong way
right way

## Slide 21: Constraint Details: Example
Set membership Operator: inside
  If other constraints are absent, all values have an equal probability of being chosen by the inside operator
  The negated (!) form of inside operator denotes that expression lies outside the set
addr is between 0 to 100
or between 1024 to 16384
class Bus
rand bit[15:0] addr;
randc bit[31:0] data;
constraint range1
{
addr inside {[0:100],[1024:16384]};
data > 1000;
data < 10000;
}
endclass
multiple mutually exclusive
constraints can be defined
within one constraint
Example: Constraint example with inside operator

## Slide 22: Constraint Details: Quiz
Declare constraint blocks c1,c2,c3 and c4 so that variable x, a and v get the values shown:
rand integer x,y,z;
constraint c1 {x inside {3,5,[9:15],[24:32];}
constraint c1 {x inside {3,5,[9:15],[24:32],[y:2*y],z};}
rand integer a,b,c;
constraint c2 {a inside {b,c};}
integer fives[0:3] = {5,10,15,20};
rand integer v;
constraint c3 {v inside fives;}
constraint c4 !{v inside fives;}
x takes any values described in the constraint_block :
x is: 3,5,9,10,11,12,13,14,15,24,25,26,27,28,29,30,31,32
x is: 3,5,9,10,11,12,13,14,15,24,25,26,27,28,29,30,31,32, between y and 2y, z
b<=a and a<=c or b<=a<=c
c3: v is either 5,10,15,20
c4: v is never 5,10,15,20

## Slide 23: Weighted Distribution
In constraint blocks, we can control the occurrence or repetition of the same value on randomization using dist operator.
Some values can be allocated more often to a random variable. This is called as weighted distribution. Weights will be specified to the values inside the constraint block.
Dist operator takes a list of values and weights, separated by := or :/

## Slide 24: Weighted Distribution
Distributions: dist operator
  Used to weigh some values more than the others
    Property 1: They are a relational test for set membership
    Property 2: They specify a statistical distribution function for the result
  Can use := or :/ operator
    := specifies that the weight has to be the same for every specified value in the range
    :/ operator specifies that the weight is to be equally divided between all values. If there are n values in a range the weight is range_weight/n
  Values can be a single value or range such as [lo:hi]
  The weights are not percentage and do not have to add up to a 100
  Cannot be used with a randc
rand integer a;
constraint c1 {a inside {0,1,1,1,1,1});
c1 should be 0 once and 1 five times
rand integer a;
constraint c1 {a dist {0:=1, 1:=5}};
Error!!! wrong way
right way

## Slide 25: Weighted Distribution
Another example
rand int src, dst;
costraint c1 {
src dist {0:=40, [1:3]:=60};
dst dist {0:=40, [1:3]:/60};
}
src | weight
0 | 40/220
1 | 60/220
2 | 60/220
3 | 60/220
dst | weight
0 | 40/100
1 | 20/100
2 | 20/100
3 | 20/100
Example: Weighted random distribution with dist

## Slide 26: Weighted Distribution: Quiz
Distributions: dist operator := and :/
x dist {100:=1, 200:=2, 300:=5}
x is 100, 200 and 300 with a weight of 1,2 and 5 respectively
x!=200;
x dist {100:=1, 300:=5}
x is 100 and 300 with a weight of 1 and 5 respectively
x is never 200
x is 100, 101 , 102 with a weight of 1 each
x is 200 and 300 with a weight of 2 and 5 respectively
x dist {[100:102]:=1, 200:=2, 300:=5}
x is 100, 101 , 102 with a weight of 1/3 each
x is 200 and 300 with a weight of 2 and 5 respectively
x dist {[100:102]:/1, 200:=2, 300:=5}

## Slide 28: Bidirectional Constraints
Bidirectional Constraints
  Constraint blocks are not procedural but declarative
    All active at one time
b | c | d
26 | 26 | 27
26 | 26 | 28
26 | 26 | 29
27 | 27 | 28
27 | 27 | 29
28 | 28 | 29
rand logic [15:0] b,c,d;
costraint c1 {
b<d;
c==b;
d<30;
c>=25;
}
30>d>b==c>=25
Solution
A
B
C
D
E
F
Solve the constraint
Example: Bidirectional constraints
Solutions for Bidirectional Constraints

## Slide 29: Conditional Constraints
Conditional constraint operators
  Constraint provide two constructs for declaring conditional relations
    Implication operator ->
    if…else
mode == small -> len<10;
mode == large -> len>100
bit [3:0] a,b;
constraint c {(a==0)->(b==1);}
if(mode==small)
len<10;
else if (mode==large)
len>100;
bit [3:0] a,b;
if(a==0)
b==1;
Example: if…else example
Example: Equivalent implication example
Example: if…else example
Example: Equivalent implication example

## Slide 30: Solution Probabilities
Unconstrained
  Probability of distribution
class Unconstrained;
rand bit x;
rand bit [1:0] y;
endclass
Solution | x | y | Probability
A | 0 | 0 | 1/8
B | 0 | 1 | 1/8
C | 0 | 2 | 1/8
D | 0 | 3 | 1/8
E | 1 | 0 | 1/8
F | 1 | 1 | 1/8
G | 1 | 2 | 1/8
H | 1 | 3 | 1/8
There are 8 possible solutions and because there are no constraints each has the same probability
Example: Class with unconstrained random variables
Solutions for Unconstrained class

## Slide 31: Solution Probabilities
Implication
  Probability of distribution changes due to the implication operator
  Implication is bidirectional
class Imp1;
rand bit x;
rand bit [1:0] y;
constraint c_xy {
(x==0)->y==0;
}
endclass
Solution | x | y | Probability
A | 0 | 0 | 1/2
B | 0 | 1 | 0
C | 0 | 2 | 0
D | 0 | 3 | 0
E | 1 | 0 | 1/8
F | 1 | 1 | 1/8
G | 1 | 2 | 1/8
H | 1 | 3 | 1/8
Value of y depends on x. When x is 0, y is 0. Hence for x=0, y cannot have any other value and hence the probability of x=0 and y!=0 is 0
Example: Class with implication
Solutions for Imp1 class

## Slide 32: Solution Probabilities
Implication and bidirectional constraints
  Probability of distribution changes due to an addition constraint
class Imp_Bid;
rand bit x;
rand bit [1:0] y;
constraint c_xy {
y>0;
(x==0)->y==0;
}
endclass
Solution | x | y | Probability
A | 0 | 0 | 0
B | 0 | 1 | 0
C | 0 | 2 | 0
D | 0 | 3 | 0
E | 1 | 0 | 0
F | 1 | 1 | 1/3
G | 1 | 2 | 1/3
H | 1 | 3 | 1/3
When x is 0, y is 0 but when y is 0 there is no constraint on x. Since implication is bidirectional, if y was forced to a non zero value, x would have to be 1. Hence x can never be 0.
Example: Class with implication and constraint
Solutions for Imp_Bid class

## Slide 33: Solution Probabilities
Solve…before
  Solve…before does not change the solution space but changes the probability of the results
class SolveBefore;
rand bit x;
rand bit [1:0] y;
constraint c_xy {
(x==0)->y==0;
solve y before x;
}
endclass
Example: Class with implication and solve…before

## Slide 34: Solution Probabilities
class SolveBefore;
rand bit x;
rand bit [1:0] y;
constraint c_xy {
(x==0)->y==0;
solve y before x;
}
endclass
Solution | y | x | Unconstrained Probability | Solution Possibility | Probability
A | 0 | 0 | 1/8 |  | 1/8
B | 0 | 1 | 1/8 |  | 1/8
C | 1 | 0 | 1/8 |  | 0
D | 1 | 1 | 1/8 |  | 1/4
E | 2 | 0 | 1/8 |  | 0
F | 2 | 1 | 1/8 |  | 1/4
G | 3 | 0 | 1/8 |  | 0
H | 3 | 1 | 1/8 |  | 1/4
Example: Class with implication and solve…before
Solutions for solve y before x constraint

## Slide 35: Solution Probabilities
Solve…before
  Solve…before does not change the solution space but changes the probability of the results
class SolveBefore;
rand bit x;
rand bit [1:0] y;
constraint c_xy {
(x==0)->y==0;
solve y before x;
}
endclass
Solution | y | x | Probability
A | 0 | 0 | 1/8
B | 0 | 1 | 1/8
C | 1 | 0 | 0
D | 1 | 1 | 1/4
E | 2 | 0 | 0
F | 2 | 1 | 1/4
G | 3 | 0 | 0
H | 3 | 1 | 1/4
Example: Class with implication and solve…before
Solutions for solve y before x constraint

## Slide 36: Solution Probabilities
Solve…before
class Imp4;
rand bit x;
rand bit [1:0] y;
constraint c_xy {
(x==0)->y==0;
solve x before y;
}
endclass
Solution | x | y | Probability
A | 0 | 0 | 1/2
B | 0 | 1 | 0
C | 0 | 2 | 0
D | 0 | 3 | 0
E | 1 | 0 | 1/8
F | 1 | 1 | 1/8
G | 1 | 2 | 1/8
H | 1 | 3 | 1/8
Example: Class with implication and solve…before
Solutions for solve x before y constraint

## Slide 37: Constraints
Iterative constraints
  Allows arrayed variables to be constrained in a parameterized manner using loop variables
class C;
rand byte A[4];
constraint C1{ foreach (A[i]) A[i]inside {2,4,8,16};}
constraint C2{ foreach (A[j]) A[j]> 2*j;}
endclass
C1 constraints each element of an array to be in the set [2,4,8,16]
C2 constraints each element of an array to be greater than twice its index

## Slide 38: Constraints
Iterative constraints
bit [3:0][2:1] B [5:1][4]
2
3
4
3
2
1
0
2
1
int A [2][3][4];
foreach (A[i,j,k])…
foreach (B[q,r,,s])…
i iterates from 0 to 1
j iterates from 0 to 2
k iterates from 0 to 3
q iterates from 5 to 1
r iterates from 0 to 3
s iterates from 2 to 1
5:1
4

## Slide 39: Constraints
Functions in constraints
  Some properties are unwieldy or impossible to express in a single expression
    For instance computing the sum of one’s in a packed array uses a loop
    Without the loop the loop will have to be unrolled
  SystemVerilog allows constraint expressions to include function calls
    Functions cannot contain output or ref arguments
    Functions should be automatic
    Functions that appear in constraints cannot modify the constraints
    Functions shall be called before constraints are solved, and their return values shall be treated as state variables
    Random variables used as function arguments shall establish an implicit variable ordering or priority
class B;
rand int x,y;
constraint C{x<=F(y);}
constraint D{ y inside {2,4,8};}
endclass
Forces y to be solved before x

## Slide 40: Constraints
Constraint guards
  Constraint guards are predicate expressions that function as guards against creation of constraints
    They are not logical relations that have to be satisfied by the constraint solver
    Prevents the solver from generating evaluation errors
  Constraint guards are solved before the constraints and involve
    Constants
    State variables
    Object handle comparisons
class SList;
rand int n;
constraint sort{n<next.n;}
endclass
The constraint will fail on the last element due to a non existent handle in the linked list
class SList;
rand int n;
constraint sort{if(next!=null)n<next.n;}
endclass
if statement acts as a constraint guard

## Slide 41: Constraints
Constraint guards
  Guard expressions can themselves include sub-expressions that result in evaluation errors
    A 4-state representation is used where
      0 : false -> Subexpression evaluates to FALSE
      1 : true -> subexpression evaluates to TRUE
      E: Error -> Subexpression causes an evaluation error
      R: Random -> Expression includes random variables and cannot be evaluated
class D
int x;
endclass
class C;
rand int x,y;
D a,b;
constraint C1{(x<y || a.x > b.x || a.x==5) -> x+y==10;}
endclass
Case | a | b | a.x | b.x | Constraint
1 | !0 | 0 | 5 | error | x+y=10
2 | 0 | - | error | - | always error
3 | !0 | !0 | 10 | 20 | ( x<y) -> (x+y==10)

## Slide 42: Constraints
Constraint guards
class D
int x;
endclass
class C;
rand int x,y;
D a,b;
constraint C1{(x<y && a.x > b.x && a.x==5) -> x+y==10;}
endclass
Case | a | b | a.x | b.x | Constraint
1 | !0 | 0 | 5 | error | error
2 | 0 | - | error | - | always error
3 | !0 | !0 | 5 | 2 | ( x<y) -> (x+y==10)

## Slide 43: Disabling Random Variables
Disabling random variables with rand_mode()
  Can be used to control whether a random variable is active or inactive
    When a random variable is inactive it implies that the variable was never declared rand or randc
    rand_mode() method is inbuilt and cannot be overridden
class Packet;
rand integer src, dst;
endclass
int r;
Packet packet_a=new;
packet_a.rand_mode(0);
packet_a.src.rand_mode(1);
r=packet_a.dst.rand_mode();
Value | Meaning | Description
0 | OFF | Sets the specified variable to inactive so that they are not randomized on subsequent calls to randomize() method
1 | ON | Sets the specified variable to active so that they are randomized on subsequent calls to randomize() method

## Slide 44: Controlling Constraints
Controlling constraints with constraint_mode()
  Can be used to control whether a constraint is active or inactive
    When a constraint is inactive is not considered by randomize()
    All constraints are initially active
    constraint_mode method is built it and cannot be overridden
class Packet;
rand integer src, dst;
constraint filter{src>2*dst;}
endclass
function integer toggle_rand (Packet p);
if (p.filter.constraint_mode()==1)
p.filter.constraint_mode(0);
else
p.filter.constraint_mode(1);
toggle_rand=p.randomize();
endfunction
Value | Meaning | Description
0 | OFF | Sets the specified constraint block to inactive so that it is not enforced by subsequent calls to randomize() method
1 | ON | Sets the specified constraint block to active so that it is considered by subsequent calls to randomize() method

## Slide 45
rand_mode method
The rand_mode() method is used to disable the randomization of a variable declared with the rand/randc keyword.
rand_mode(1) means randomization enabled
rand_mode(0) means randomization disabled
The default value of rand_mode is 1, i.e enabled
Once the randomization is disabled, it is required to make rand_mode(1) enable back the randomization
rand_mode can be called as SystemVerilog method, the randomization enables/disable .
Status of a variable can be obtained by calling vairble.rand_mode().