## Slide 1: Module3
Ch:3 Procedural Statements and Routines
Ch4: Connecting test bench and DUT

## Slide 2: System Verilog Procedural Statements
New Operators
  Increment and decrement operator
    Used the same way as C
    Post-increment/decrement and pre-increment/decrement
    May cause a race condition since ++ and -- operators behave as blocking assignments
for (i=0; i<=31; i++)
begin
…
end
j=i++
j=++i
j=i--;
j=-i;
j is assigned value of i and then i is incremented by 1
i is incremented by 1 and j is assigned value of i
j is assigned value of i and then I is decremented by 1
i is decremented by 1 and then j is assigned value of i

## Slide 3: System Verilog Procedural Statements
Enhanced for loops
  for loop variables are declared outside the loop in Verilog
    Concurrent loops interfere with each other
  SystemVerilog allows the for loop variables to be declared inside the loop
    Each variable is local and unique to the loop, hence same name usage does not cause any interference
    Local loop variables are automatic
    The variables do not exist outside the loops

## Slide 4
always @(posedge clock) begin
for(int i=1; i<=1024; i=i+1)
…
end
endmodule

## Slide 5: System Verilog Procedural Statements
do…while loop
  A while loop in Verilog might not execute at all
    If the test of control values is false the first time the loop is encountered in the execution flow
  SystemVerilog adds a do..while loop (similar to C)
    A do while loop executes atleast once
    Control of the loop is tested at the end of each pass of the loop
      All logic for setting the outputs of the loop can be placed inside the loop
      Makes code more concise and intuitive
do <statement or statement block>
while (<condition>);

## Slide 6: break and continue statements

## Slide 7: System Verilog Procedural Statements
break and continue:
The execution of a break statement leads to the end of the loop.
break shall be used in all the loop constructs (while, do-while, foreach, for, repeat and forever).
Execution of continue statement leads to skip the execution of statements followed by continue and jump to next loop or iteration value

## Slide 8: Example for break statement
module break_in_loop;
initial begin
$display("-----------------------------------------------------------------");
for(int i=0;i<8;i++) begin
$display("\tValue of i=%0d",i);
if(i == 4) begin
$display("\tCalling break,");
break;
end
end
$display("-----------------------------------------------------------------");
end
endmodule
when the loop value equals 4, the break is called this leads to the end of the loop.

## Slide 9: Example for continue statement
module continue_in_loop;
initial begin
$display("-----------------------------------------------------------------");
for(int i=0;i<8;i++) begin
if((i > 2) && (i < 7))begin
$display("\t\tCalling continue,");
continue;
end
$display("\t\tAfter Continue\t:: Value of i=%0d",i);
end
$display("-----------------------------------------------------------------");
end
Endmodule
when ever the loop value is with in 3 to 6, continue statement will be executed, this leads to skip the execution of display statement after the continue.

## Slide 10: Tasks and functions
Tasks and Functions provide a means of splitting code into small parts.
A Task can contain a declaration of parameters, input arguments, output arguments, in-out arguments, registers, events, and zero or more behavioral statements.
Static tasks
Static tasks share the same storage space for all task calls.
Automatic tasks
Automatic tasks allocate unique, stacked storage for each task call.

## Slide 11
Task declration can be as in verilog 1995/2001 or can be declared as in C or C++. In SystemVerilog following rules hold good for any Task declaration
Default Port Direction : Any port is seen as input, unless declared as other types. Following are port types
input : copy value in at beginning
output : copy value out at end
inout : copy in at beginning and out at end
ref : pass reference

## Slide 12
Default Data TYpe : Unless declared, data types of ports are of logic type.
begin..end : There is no need to have begin, end, when more then one statement is used.
return : A task can be terminated before endtask, by usage of return statement.
Variables : Systemverilog allows to have local static, or local dynamic variables.
life time : SystemVerilog allows a task to static or automatic.
wire : Wire data type can not be used in port list;

## Slide 13: task arguments in parentheses
module sv_task;
int x;
//task to add two integer numbers.
task sum(input int a,b,output int c);
c = a+b;
endtask
initial begin
sum(10,5,x);
$display("\tValue of x = %0d",x);
end
endmodule

## Slide 14: task arguments in declarations and mentioning directions
module sv_task;
int x;
//task to add two integer numbers.
task sum;
input int a,b;
output int c;
c = a+b;
endtask
initial begin
sum(10,5,x);
$display("\tValue of x = %0d",x);
end
endmodule

## Slide 15: Functions
A Function can contain declarations of range, returned type, parameters, input arguments, registers, and events.
A function without a range or return type declaration returns a one-bit value
Any expression can be used as a function call argument
Functions cannot contain any time-controlled statements, and they cannot enable tasks
Functions can return only one value

## Slide 16
Function declration can be as in verilog 1995/2001 or can be declared as in C or C++. In SystemVerilog following rules hold good for any Function declaration
Default Port Direction : Any port is seen as input, unless declared as other types. Following are port types
input : copy value in at beginning
output : copy value out at end
inout : copy in at beginning and out at end
ref : pass reference

## Slide 17
Default Data TYpe : Unless declared, data types of ports are of logic type.
begin..end : There is no need to have begin, end, when more then one statement is used.
return : A function can be terminated before endfunction, by usage of return statement.
Variables : Systemverilog allows to have local static, or local dynamic variables.
life time : SystemVerilog allows a function to static or automatic.
Wire : Wire data type can not be used in port list;
void : SystemVerilog allows functions to be declared as type void

## Slide 18: function arguments in parentheses
module sv_function;
int x;
//function to add two integer numbers.
function int sum(input int a,b);
sum = a+b;
endfunction
initial begin
x=sum(10,5);
$display("\tValue of x = %0d",x);
end
endmodule

## Slide 19: function arguments in declarations and mentioning directions
module sv_function;
int x;
//function to add two integer numbers.
function int sum;
input int a,b;
sum = a+b;
endfunction
initial begin
x=sum(10,5);
$display("\tValue of x = %0d",x);
end
endmodule

## Slide 20: function with return value with the return keyword
module sv_function;
int x;
//function to add two integer numbers.
function int sum;
input int a,b;
return a+b;
endfunction
initial begin
x=sum(10,5);
$display("\tValue of x = %0d",x);
end
endmodule

## Slide 21: Void function
module sv_function;
int x;
//void function to display current simulation time
function void current_time;
$display("\tCurrent simulation time is %0d",$time);
endfunction
initial begin
#10;
current_time();
#20;
current_time();
end

## Slide 22: discarding function return value
The function return value must be assigned to a variable or used in an expression.
Calling a function without return value assigned to a variable can result in a warning message. SystemVerilog void data type is used to discard a function’s return value without any warning message.

## Slide 23
module sv_function;
int x;
//function to add two integer numbers.
function int sum;
input int a,b;
return a+b;
endfunction
initial begin
$display("Calling function with void");
void'(sum(10,5));
end
endmodule

## Slide 24: function call as an expression
module sv_function;
int x;
//function to add two integer numbers.
function int sum;
input int a,b;
return a+b;
endfunction
initial begin
x = 10 + sum(10,5);
$display("\tValue of x = %0d",x);
end
endmodule

## Slide 25: SystemVerilog Tasks and Functions
Tasks and Functions
  SystemVerilog functions and tasks do not require begin and end statements
  SystemVerilog adds a return statement
  Void functions do not return a value
  Functions can have output and inout as formal arguments
task reset();
reset_l = 1’b0;
#100
reset_l = 1’b1;
endtask
function int add2(int n);
return n + 2;
endfunction

## Slide 26: SystemVerilog Tasks and Functions
Return Statement
  SystemVerilog adds a return statement
    If a return statement is executed that value is returned else the last value assigned to the function name is the return value
    A return statement can be used to exit a task or a function
function int add_and_inc (input [31:0] a,b);
add_and_inc=a+b+1;
endfunction
function int add_and_inc (input [31:0] a,b);
add_and_inc=a+b;
return ++add_and_inc;
endfunction
Return has priority over returning the value in the name of the function

## Slide 27: SystemVerilog Tasks and Functions
Void functions
  Void functions do not return a value
  Output and inout formal arguments allow a void function to propagate changes to the scope
  A void function can be called like a task but must adhere to the restriction of function contents

## Slide 28
typedef struct{
logic valid;
logic [7:0] check;
logic [63:0] data;
} packet_t;
function void fill_packet (
input logic[63:0] data_in, output packet_t data_out);
data_out.data=data_in;
endfunction

## Slide 29: SystemVerilog Tasks and Functions
Passing task/function arguments by name
  SystemVerilog can pass argument values to tasks or functions using the names of formal arguments
    Reduces errors
  The arguments can be passed in any order
  Syntax for named argument passing is the same as Verilog’s syntax for named port connections

## Slide 30
function int divide (input int numerator, denominator);
if(denominator==0)
begin
return 0;
end
else
return numerator/denominator;
endfunction
always @(posedge clock)
result<=divide(b,a)
always @(posedge clock)
result<=divide(.deominator(b),.numerator(a))

## Slide 31: Connecting the Testbench and the Design
How do I connect my design to the testbench?
Design Under Test
Driver
Testbench
?
.*Port, .Name,
Interfaces

## Slide 32: Connecting the Testbench and the Design
One way to connect the testbench and the design is to use the conventional verilog module ports convention
Module A
Module B
module A (
input A_in_signal1,
input A_in_signal2
output A_out_signal1,
output A_out_signal2,
);
…
endmodule
module B (
input B_in_signal1,
input B_in_signal2
output B_out_signal1,
output B_out_signal2,
);
…
endmodule
B_in_signal1
A_out_signal1
B_in_signal2
A_out_signal2
B_out_signal1
A_in_signal1
B_out_signal2
A_in_signal2
Verilog Connection Review

## Slide 33: Connecting the Testbench and the Design
Verilog connection review
  Verilog language connects modules together through module ports
module top (
wire conn1,
wire conn2
wire conn3,
wire conn4,
);
A A_instance1(.A_out_signal1(conn1),
.A_out_signal2(conn2),
.A_in_signal1(conn3),
.A_in_signal2(conn4));
B B_instance1(.B_in_signal1(conn1),
.B_in_signal2(conn2),
.B_out_signal1(conn3),
.B_out_signal2(conn4));
endmodule
Module A
Module B
B_in_signal1
A_out_signal1
B_in_signal2
A_out_signal2
B_out_signal1
A_in_signal1
B_out_signal2
A_in_signal2
conn1
conn2
conn3
conn4

## Slide 34: Connecting the Testbench and the Design
Lets do another example:
Arbiter
request [1:0]
Testbench
reset
grant [1:0]
clk
module arb_port (
output logic [1:0] grant,
input logic [1:0] request,
input logic reset,
input logic clk
);
…
endmodule
module test (
input logic [1:0] grant,
output logic [1:0] request,
output logic reset,
input logic clk
);
…
endmodule

## Slide 35: SystemVerilog: .*Port Connections
Implicit .* port connections
  .* infers connections of all nets and ports of the same name
  For a connection to be inferred the name and the vector sizes should be the same
  Types connected together should be compatible
module top
logic [1:0] grant,request;
logic clk, reset;
arb_port a1(.*);
test t1(.*);
…
endmodule
module top
logic [1:0] grant,request;
logic clk, reset;
arb_port a1(.grant(grant), .request(request), .reset(reset), .clk(clk));
test t1(.grant(grant), .request(request), .reset(reset), .clk(clk));
…
endmodule
.*Port Connections

## Slide 36: SystemVerilog: .Name Connections
Implicit .name connections
  .name is an abbreviation of named port connections
  .name infers a connection of a net and port of the same name and same vector sizes
  .name simplifies connections to module instances
  .name can be combined with named port connections
module top
logic [1:0] grant,request;
logic clk, reset;
arb_port a1(.grant, .request, .reset, .clk);
test t1(.grant, .request, .reset, .clk);
…
endmodule

## Slide 37: Downside of Verilog Connection Conventions
Verilog module port conventions are cumbersome
module arb_port (
output logic [1:0] grant,
input logic [1:0] request1,
input logic reset,
input logic clk
);
…
endmodule
module test (
input logic [1:0] grant,
output logic [1:0] request1,
output logic reset,
input logic clk
);
…
endmodule
Lets change the name of a port request to request 1
Why?
Need to change the port list of each module
Need to change the port list of the connecting module
Need to change the name in the instantiation of the modules
Need to change the name everywhere in the hierarchy
What if you forget to change it in someplace?? --> Compilation error!!!!

## Slide 38: Downside of Verilog Connection Conventions
Verilog connections become especially tedious and cumbersome for large designs
Internal
Memory
Instruction Fetch
Master Processor
Test Generator
Slave Processor
main bus
10
10
15
10
10
10
Number of ports

## Slide 39: Disadvantages of Verilog Connection Conventions
Disadvantage of Verilog Module Connections
  Declarations must be duplicated in multiple modules
  Communication protocols must be duplicated in several modules
  Risk of mismatched declarations
  A change in design specifications can require modifications in multiple modules
SystemVerilog introduces a powerful new port type called: Interface
Solution!!!!

## Slide 40: SystemVerilog Interfaces
SystemVerilog Interfaces
  SystemVerilog adds a powerful new port type to Verilog, called an interface.
  An interface allows a number of signals to be grouped together and represented as a single port
  The declarations of the signals that make up the interface are contained in a single location.
  Each module that uses these signals then has a single port of the interface type, instead of many ports with the discrete signals.
Testbench
Arbiter
Interface
All the signals that are common between the major blocks of the design are encapsulated in one location- the interface declaration

## Slide 41: SystemVerilog Interfaces
Testbench
Arbiter
Interface
interface arb_if (input bit clk);
logic [1:0] grant, request;
logic reset;
endinterface
clk
request [1:0]
reset
grant [1:0]
Interface
Using an interface to simplify connections
Interface Declaration
module top;
bit clk;
always #5 clk=~clk;
arb_if arbif(clk);
arb a1(arbif);
test t1(arbif);
endmodule: top
Top module using a simple arbiter interface

## Slide 42: SystemVerilog Interfaces
interface arb_if (input bit clk);
logic [1:0] grant, request;
logic reset;
endinterface
Using an interface to simplify connections
Interface Declaration
module test (arb_if arbif);
…
initial begin
@(posedge arbif.clk);
arbif.request<=2’b01;
$display (“@%0d: Drove req=01”, $time);
repeat(2) @(posedge arbif.clk);
if(arbif.grant!=2’b01)
$display (“@%0d: a1: grant !=2’b01”, $time);
$finish
end
endmodule: test
test module using a simple arbiter interface

## Slide 43: SystemVerilog Interfaces
interface arb_if (input bit clk);
logic [1:0] grant, request;
logic reset;
endinterface
Connecting interfaces and ports
  Signals in an interface are referenced using the port name
Interface Declaration
module top;
bit clk;
always #5 clk=~clk;
arb_if arbif(clk);
arb a1(.grant(arbif.grant),
.request(arbif.request),
.reset(arbif.reset),
.clk(arbif.clk));
test t1(arbif);
endmodule: top
Connecting the arbiter module using ports to the test module using an interface
<port_name>.<internal_interface_signal_name>

## Slide 44: SystemVerilog Interfaces: modports
Interface modports
  SystemVerilog interfaces provide a means to define different views of the interface signal
  modport is an abbreviation for module port
  An interface can have any number of modport definitions
  The modport declaration only defines whether the connecting module sees a signal as an input, output or bidirectional
  By specifying the port directions, modport provides access restrictions
interface arb_if (input bit clk);
logic [1:0] grant, request;
logic reset;
modport TEST(output request,reset,
input grant, clk);
modport DUT(input request,reset, clk
output grant);
endinterface
module arb (abf_if.DUT arbif);
…
endmodule
1. Interface Declaration using modports
2. arbiter module with interface using modports
module test (abf_if.TEST arbif);
…
endmodule
3. test module with interface using modports

## Slide 45: SystemVerilog Interfaces
SystemVerilog interfaces overview
  SystemVerilog interfaces can contain functionality
    They are not just bundle of wires
    Discrete signal and ports for communications can be defined in one location
    Communication protocols can be defined in the interface
    Protocol checking and other verification routines can be built into the interface
  SystemVerilog also allows multiple views of the interface to be defined
    For instance the data_bus signal can be defined to be an input, output or bidirectional port
  SystemVerilog interfaces cannot contain design hierarchy
    cannot contain instances of modules
  SystemVerilog interfaces can be used as a module port
  SystemVerilog interfaces can contain modports
    modports allow modules to see interface differently

## Slide 46: System verilog modports-example code
//Defining modport in interface
interface intf();
//declaring the signals
logic [3:0] a;
logic [3:0] b;
logic [6:0] c;
modport driver (output a, b, input c);
endinterface
//driving using modort
//run task
task run;
vif.driver.a = 6;
vif.driver.b = 4;
$display("Value of a = %0d, b = %0d",vif.driver.a,vif.driver.b);
#5;
$display("Sum of a and b, c = %0d",vif.driver.c);
$finish;
Endtask
Simulator output:
Value of a = 6, b = 4 Sum of a and b, c = 10

## Slide 47: Example2
//Defining modport in interface with the direction input
interface intf();
//declaring the signals
logic [3:0] a;
logic [3:0] b;
logic [6:0] c;
modport driver (input a, b, c);
endinterface
//driving using modport
//run task
task run;
vif.driver.a = 6;
vif.driver.b = 4;
$display("Value of a = %0d, b = %0d",vif.driver.a,vif.driver.b);
#5;
$display("Sum of a and b, c = %0d",vif.driver.c);
$finish;
Endtask
Simulation output:
Error-[MPCBD] Modport port cannot be driven environment.sv, 18 $unit, "vif.driver.a" Port 'a' of modport 'driver' has been restricted as an input port. Input ports cannot be driven.

## Slide 48: Stimulus Timing
10
42
start
write
addr
5a
data
10
42
start
write
addr
5a
data
Tsetup
The timing between the testbench and the design should be maintained to avoid race conditions
Driving the signal too late and sampling it too early causes the race condition to occur
Solution: Drive the signal Tsetup early to avoid race condition

## Slide 49: When test bench drives start signal first and then other signals, race occurs.

## Slide 50: Stimulus Timing
The timing between the testbench and the design should be maintained
  Ensure driving and receiving synchronous signals at the proper time in relation to the clock
  Driving a signal too late or sampling it too early can cause the testbench to be off a cycle
  To ensure proper sampling and signaling the testbench should be separate from the design
  The inputs should be driven just before the clock edge and outputs should be sampled just after the clock edge

## Slide 51: Stimulus Timing: Clocking Blocks
Controlling timing of synchronous signals by using Clocking Blocks
  An interface may contain a clocking block to specify the timing of synchronous signals relative to the clock
    Any signal in the clocking block is driven or sampled synchronously, ensuring that the testbench interacts with the signals at the right time
    Clocking block ensures that the testbench interacts with the signals at the right time
    Clocking blocks are mainly used by testbenches
    An interface can contain multiple clocking blocks.
    Synthesis tools do not support clocking blocks.

## Slide 52: System Verilog Testbench in Simulation
  When you are using interfaces with a clocking block:
    There is a 1-cycle delay from DUT output to testbench input
      “Virtual synchronizer” added to TB input
    No delay from testbench output to DUT input
    default input #1step output #0;
clock
Sample inputs
before clock
Drive outputs
at clock
Design
Testbench

## Slide 53: Stimulus Timing: Clocking Blocks
Clocking Block
  Can be declared as @(posedge clk)
  An interface can use a clocking block to control timing
    Directions are relative to program block
reset
request[1:0]
grant[1:0]
clock
arb.sv
interface arb_if (input bit clk);
logic [1:0] grant, request;
logic reset;
clocking cb @(posedge clk);
output request
input grant
endclocking
modport TEST(clocking cb,output reset);
modport DUT(input request, reset, output grant);
endinterface
Declare the clocking block and indicate that the signals will be active on positive edge of the clock
Using the clocking block, (request is output and grant is input)
arb_if arbif;
arbif.cb.request<=2’b01;
if(arbif.cb.grant!=2’b01)
@arbif.cb
<my_interface.cb.signal_name>
Example of clocking block
Referencing signals in the Clocking Block
Example of refrencing signals in the clocking block

## Slide 54: Clocking Block: Signal Synchronization
Synchronize to active clock edge specified in clocking block
Synchronize to any edge of signal
Wait for N clock cycles with ##n
@arbif.cb; // continue on clock edge from arb_if
repeat (3) @arbif.cb; // Wait for 3 posedges
@arbif.cb.grant; // continue on any edge of grant
@(posedge arbif.cb.grant); // continue on posedge
@(negedge arbif.cb.grant); // continue on negedge
wait (arbif.cb.grant==1); // wait for expression
// no delay if already true
##2 arbif.cb.request <= 0; // Wait 2 cycles // then assign

## Slide 55: Clocking Block: Synchronous Signal Access
Clocking Block signals are referenced by pre-pending the clocking block name to the signal:
Assignment will happen at next active clock edge
  Time will NOT advance unless you use #1 or ##1
All drives must use non-blocking assignment
arbif.cb.request <= 1; // drive
value = arbif.cb.grant; // sample
interface arb_if (input bit clk);
logic grant, request, reset;
clocking cb @(posedge clk);
input grant;
output request;
endclocking
modport TB (clocking cb, output reset);
endinterface: arb_if

## Slide 56: Stimulus Timing: Clocking Blocks
Clocking Blocks overview
  Use in the interface, just for testbench
  Benefits:
    Creates explicit synchronous timing domains
    Provides race-free operation if input skew > 0
    Your testbench will always drive the signals at the right time!
  Functionality:
    An interface can contain multiple clocking blocks
    There is one clock per clocking block.
    Default is “default input #1step output #0;”
      The 1 step delay specifies that signals be sampled in the postpone region before any design activity
      Directions are with-respect-to the testbench

## Slide 57: Stimulus Timing: Timing Regions
Timing Regions
  Race conditions are caused by mixing design and testbench events during the same time slot
  SystemVerilog introduces division of time slots
    Active Region: Simulation of design code in modules
    Observed Region: Assertions evaluated after design executes
    Reactive Region: Execution of testbench
    Postpone Region: Sampling signals after all design activity
clock
data
REGION
ACTIVITY
Next
Previous
Observed
Reactive
Postpone
Active
design
assertions
testbench
sample
Current

## Slide 58: Timing Regions
Interface Synchronization
  Use @ and wait signals to synchronize with the signals
Interface Sample
  Sample from the postpone region
‘timescale 1ns/1ns
program test (arb_if.TEST arbif);
initial begin
$monitor(arbif.cb.grant);
#50
end
endprogram
module arb(arb_if.DUT arbif)
initial begin
arbif.grant=1;
#12 arbif.grant=2;
#18 arbif.grant=3;
end
endmodule
10
20
30
40
1
2
2
3
1
2
2
3
clk
DUT arb.grant
TEST arbif.cb.grant
Input is sampled just before the clock edge

## Slide 59: Timing Regions
Interface Drive
mdule arb (arb_if.DUT arbif);
initial begin
$monitor(arbif.request);
end
endprogram
‘timescale 1ns/1ns
program test(arb_if.TEST arbif)
initial begin
arbif.cb.request<=3;
#12 arbif.cb.request<=2;
#18 arbif.cb.request<=1;
end
endmodule
10
20
30
40
3
2
1
3
2
2
1
clk
DUT arbif.request
TEST arbif.cb.request
Input is sampled just before the clock edge

## Slide 60: Program Block
Program Block
  In Systemverilog the test bench code is in a program block
    Program block is similar to a module and can contain code and variables and be instantiated in other modules
    A program cannot have hierarchy such as instances of modules or interfaces
program test (arb_if.TEST arbif);
initial begin
@arbif.cb;
repeat (3) arbif.cb;
@arbif.cb.grant;
@(posedge arbif.cb.grant);
@(negedge arbif.cb.grant);
wait (arbif.cb.grant==1);
@(posedge arbif.cb.grant or negedge arbif.reset);
end
endprogram
Continue on active clock edge
Wait for 3 active edges
Continue on any edge
Continue on positive edge
Continue on negative edge
Wait for expression to be true
Wait for several signals

## Slide 61: Program Block
Create testbench program: test.sv
Wait 1 clock cycle
Common mistake: forgot “cb.” in signal reference Error: arbif.request not visible via modport
clk
reset
request
ns!
program test(arb_if.TB arbif);
initial begin
// Asynch drive reset
arbif.reset <= 0;
#15ns arbif.reset <= 1;
#35ns arbif.reset <= 0;
// Synch drive request
##1 arbif.cb.request <= 1;
##1 arbif.cb.request <= 0;
wait (arbif.cb.grant == 1);
end
endprogram
interface arb_if (input bit clk);
logic grant, request, reset;
clocking cb @(posedge clk);
input grant;
output request;
endclocking
modport TB (clocking cb,
output reset);
endinterface: arb_if

## Slide 62: Program Block Overview
Benefits:
  Separates the testbench from the DUT
  Reduces race conditions by running in separate region
  Provides an entry point for execution
  Creates a scope to encapsulate program-wide data
Functionality:
  Can be instantiated in any hierarchical location
    Typically at the top level
  Interfaces and ports can be connected in the same manner as any other module
  Code goes in initial blocks & routines, no always blocks
  Executes in the Reactive region
  Implicit $finish when all initial blocks end in program

## Slide 63: Testbench Environment – Top Block
Create top module
Implicit port connections:
The syntax .* connect ports
and signals with same names
Generate clock in top module (Active region)
vs. program (Reactive) to prevent races.
Your design is tied tightly to the clock,
so they need to be in the same region.
module top;
bit clk;
arb_if arbif(.*);
test t1 (.*);
arb d1 (.*);
always #5
clk = !clk;
endmodule
interface arb_if (input bit clk);
…
endinterface: arb_if
// Synchronous TB
program test(arb_if.TB arbif);
…
endprogram
module arb(arb_if.DUT arbif,
bit clk);
// Some logic here…
endmodule

## Slide 64: Top Level Scope
SV introduces a compilation unit scope referred as $unit.
$unit contains a group of source files that are compiled together.
This scope is present outside the boundaries of any primitive, module, macro module, interface, program,package etc.